## Slide 1: 4-Bit RISC CPU with a 3-Stage Pipeline
Verilog HDL project
Design, implementation and verification
Pham Chi Thien – HE200499

## Slide 2: Key specifications
Datapath
4-bit registers, ALU and data memory
Registers
4 general-purpose, R0 to R3
Instructions
12 bits: opcode, Rd, Rs, 4-bit immediate
Memory
Harvard: 16 x 12-bit program, 16 x 4-bit data
Control
Hardwired decoder and branch unit
Flags
Zero and Carry (no-borrow on SUB)

## Slide 3: Datapath blocks by stage
IF
PC and PC + 1
PC MUX
Instruction memory
IF/ID register (IR)
ID
Control unit (decoder)
ID/EX pipeline register
EX
Register file, operand MUX
ALU and flag register
Data memory, write-back MUX
Branch unit
The branch unit sends pc_sel and flush back to IF when a jump is taken.

## Slide 4: Three stages, one instruction per clock
IF: fetch
PC addresses instruction memory; the instruction is loaded into the IR
ID: decode
Hardwired decoder turns the opcode into control signals
EX: execute
Register read, ALU, data memory and write-back
N instructions take N + 2 clocks. A taken jump flushes 2 instructions.

## Slide 5: 4 instructions in 6 clocks
I1
I2
I3
I4
IF
ID
EX
IF
ID
EX
IF
ID
EX
IF
ID
EX
Clocks 1 to 6 run left to right. From clock 3, one instruction finishes every clock.
Without a pipeline the same 4 instructions need 12 clocks.

## Slide 6: Pipeline hazards without stalls
Structural
Separate instruction and data memories (Harvard)
Data
Registers are read in EX, one clock after the previous write
Control
Jump decided in EX; the 2 wrong instructions are flushed

## Slide 7: 12 instructions, one 12-bit format
Arithmetic
ADD, SUB (Zero and Carry)
Logic
AND, OR, XOR, NOT
Data
LDI, MOV, LOAD, STORE
Control
JMP, JZ
Bits 11-8 opcode, 7-6 Rd, 5-4 Rs, 3-0 imm or address. Example: ADD R1, R2 = 0x060.

## Slide 8: Reading a 12-bit instruction
opcode
bits 11-8
Rd
bits 7-6
Rs
bits 5-4
imm / addr
bits 3-0
ADD R1, R2
0000 01 10 0000 = 0x060
LDI R3, 1010
0110 11 00 1010 = 0x6CA
JZ 9
1011 00 00 1001 = 0xB09

## Slide 9: Control unit: decoder and branch unit
Decoder (ID stage)
Combinational, with safe "do nothing" defaults
Reserved opcodes 1100-1111 act as NOP
LDI sets alu_src_sel, LOAD sets wb_sel, STORE sets mem_we
Branch unit (EX stage)
Not a jump: pc_sel = 0, flush = 0
JMP: pc_sel = 1, flush = 1
JZ with Zero = 1: pc_sel = 1, flush = 1
JZ with Zero = 0: no loss

## Slide 10: ALU flags and the carry convention
ADD: Carry = 1 when the sum does not fit in 4 bits. SUB: Carry = 1 means no borrow (A >= B), as on ARM.
5 + 3
1000, Zero 0, Carry 0: fits in 4 bits
15 + 1
0000, Zero 1, Carry 1: overflow
5 - 3
0010, Zero 0, Carry 1: no borrow
3 - 5
1110, Zero 0, Carry 0: borrow
7 - 7
0000, Zero 1, Carry 1: zero, no borrow

## Slide 11: Verification results
88 / 88
self-checking tests passed
11
ALU
11
Register file
22
Control unit
44
Full CPU
1.4x to 1.7x fewer clocks than the earlier 2-cycle design on the test programs.

## Slide 12: Limitations and extensions
Taken jump costs 2 clocks: decide JMP in ID or add branch prediction
16 instructions and 16 data words: wider PC, register-indirect LOAD
One conditional jump: use reserved opcodes for JC, JNZ, HALT
No V or N flags, no subroutines: add CALL and RET